## Slide 1
6th International Mine Rescue Conference, Niagara Falls
Where Next for Self-Escape and Rescue? David Brenkley & Robert Jozefowicz Mines Rescue Service Limited, United Kingdom

## Slide 2: Theme of Presentation: 1. Current circumstances of the industry; Scene setting, review of self-escape and rescue issues, industry recommendations, required research areas. 2. Addressing secondary explosion risk Concept of explosion protected sensors and ‘safety capable’ underground network infrastructure with adaptive behaviour and high survivability prospects.

## Slide 3: Scene Setting
Modern mines planned for high production levels
Mines increasingly operate at significant depth
Travelling distances significant
Coal face and retreat panel dimensions increasing (>350m face width, >3km panel length)
High power equipment, dust suppression, longer running periods increase waste heat energy and humidity
Environmental control problems can be severe
Ventilation circuit extension is a major issue
Questions over early fire detection capability
Questions over wired infrastructure resilience
Questions over how heat, humidity and smoke affect evacuation and rescue capability

## Slide 4
Common issues with an international dimension:
5. Secondary explosion risks
6. Impacts of heat and humidity
1. Information deficiencies and poor situational awareness
2. Poor communications infrastructure resilience
3. Location and status of workforce
4. Delays in rescue initiation
Review of previous IMRB conferences…

## Slide 5: Research Issues in Self-Escape and Rescue
Very much a personal view but suggest following important:
How do we assess secondary explosion risk and possible 'windows of opportunity' in order to commit rescue teams?
How do we safely increase the 'penetration distance' envelope limitations imposed on rescuers due to heat and humidity?
How do we access inbye refuges in severe, deteriorating conditions?
Can we provide zonal protection strategies to protect escapeways (and refuges) from heat and smoke effects?
How do we advance the state of escape respiratory protection, possibly exploiting the best features of SCSRs and FSRs?

## Slide 6: Research Issues in Self-Escape and Rescue
Today’s presentation focusses on reducing secondary explosion risks associated with mine re-entry. Other research areas considered noteworthy:
  Water mist technologies applied to open fires and heatings (using specialist additives).
  Zonal mist systems used to cool and protect escapeways.
  High cooling capacity borehole ventilation schemes with delivery to >3000m using intercooled compressors.
  Evacuation modelling and real-time support tools for assessing self-escape routes, affected mine areas and tenability.
  Advanced emergency location and communication systems with long range strata penetration capabilities.
  Further ideas on navigation through smoke, personnel location and tracking.

## Slide 7
US NATIONAL ACADEMY RECOMMENDATIONS:
ASSESSMENT OF EMERGENCY RESPONSE:
Conduct at least annually a comprehensive self-escape scenario exercise at every underground mine.
The scenario should test all aspects of the mine's emergency response plan.
Reviews of effectiveness of emergency response systems should be shared with all personnel involved.
Outcomes and lessons learned should be entered into a public database.

## Slide 8
US NATIONAL ACADEMY RECOMMENDATIONS:
TECHNOLOGY:
Review emergency breathable air supplies. Research required; to improve verbal communications, device weight/size, changeover/recharge, fit testing and vision for wearer.
Accelerate other self-escape technologies. Focus on improving situational awareness and decision making. To include:
- communications, both miner to miner and miner to surface;
- real-time gas monitors;
- fail-safe tracking that is hardened and survivable; and
- multifunction devices with reduced physical burden and attention demands.

## Slide 9
US NATIONAL ACADEMY RECOMMENDATIONS:
TECHNOLOGY:
Reduce/eliminate barriers to technology transfer. Explore opportunities to harmonise international standards.
DECISION SCIENCE:
Improve knowledge and situational awareness of warning signs and unexpected events. Train miners using standard protocols.
SAFETY CULTURE:
Assess practices and recommendations from other high hazard industries. Produce better tools to analyse organisation's strengths and weaknesses. Benchmark activities.

## Slide 10
US NATIONAL ACADEMY RECOMMENDATIONS:
TRAINING:
Analyse knowledge, skills, abilities required for self-escape. Review current training facilities. Identify gaps. Examine self-escape simulation and scenario training needs. Verify effectiveness of training and retention of information learned under simulated emergency conditions.
OVERALL CONCLUSIONS:
Emergency response plans need to be fully integrated and based on a human-systems integration approach. Ensure active engagement between miners, mine operators and technology suppliers.

## Slide 11: Addressing Secondary Explosion Risk
Underground incidents involving infrastructure damage
Is there a “window of opportunity”?
What are the critical information requirements?
Ideas for a resilient monitoring capability
Ideas for resilient communications

## Slide 12: Addressing Secondary Explosion Risk
Underground incidents involving infrastructure damage
Is there a “window of opportunity”?
What are the critical information requirements?
Ideas for a resilient monitoring capability
Ideas for resilient communications

## Slide 13
Most mines employ telephones, intercoms (Tannoys), leaky feeder radio and SCADA systems. Some mines use wireless networks and wired Ethernet networks.
Installed systems, with traditional point-to-point cables, are unable to fulfil the requirements for resilience and functional safety.
One limitation is the use of a single-ended or a ‘star’ topology of point-to-point cabling. If a ‘backbone’ cable is destroyed then all parts of the mine supplied from the critical node will lose communications.
As far as we can determine, there is no formal methodology employed in the mining industry to assess the safety and resilience of critical mining communications infrastructure .

## Slide 14: Fire damage at Warndt-Luisenthal mine, Germany (2004)

## Slide 15: Explosion damage at Westray mine, Nova Scotia (1992)

## Slide 16: Explosion damage at Pike River mine, New Zealand

## Slide 17: Addressing Secondary Explosion Risk
Underground incidents involving infrastructure damage
Is there a “window of opportunity”?
What are the critical information requirements?
Ideas for a resilient monitoring capability
Ideas for resilient communications

## Slide 18
Following an explosion in a coal mine, commentators often propose that the best time to enter the mine is immediately following the initial explosion.
If mines rescue service do not re-enter the mine at this time, their action (or lack of action) can therefore be questioned.
However, the idea that there is a ‘window of opportunity’ to enter a mine immediately after an explosion is based largely on the assumption that the gases have been consumed and will take time to build up again, to an explosive level.
A defensible view is that there is no reliable natural ‘window of opportunity – there are a number of recorded incidents where rescue workers have been killed by secondary explosions.
Brady and Cliff (2012) reviewed times to subsequent explosion, which were between minutes and days.

## Slide 19
Period between explosions at different mines *
0–5 min Castle Gate No. 2 Mine, Willow Creek
5–10 min Willow Creek
10–20 min Castle Gate No. 2 Mine, Robena No. 3, Eccles No. 5 & 6
30–60 min Jim Walter Resources No. 5 Mine
1–3 hours Consol No. 5 Mine, Sayreton No. 2 mine
3–6 hours Bilsthorpe Colliery, Raspadskaya Mine, Consol No. 9 Mine
6–12 hours Pond Creek No. 1 Mine, Consol No. 9 Mine
12–24 hours Consol No. 9 Mine
1–2 days Consol No. 9 Mine
2–3 days Scotia Mine, Moura No. 2, Pike River Mine
3+ days Consol No. 9 Mine, Pike River Mine
* Brady and Cliff, 2012. Opportunity for re-entry into a coal mine immediately following an explosion. University of Wollongong 2012 Coal Operators’ Conference, 16–17 February 2012, pp335–339

## Slide 20: Addressing Secondary Explosion Risk
Underground incidents involving infrastructure damage
Is there a “window of opportunity”?
What are the critical information requirements?
Ideas for a resilient monitoring capability
Ideas for resilient communications

## Slide 21
Mine rescue is best served when decisions are based on appropriate data concerning the toxicity of the atmosphere and the potential for secondary explosions or fires.
We need to use a risk assessment that is based on reliable knowledge of the mine atmosphere. See example of New South Wales guidelines below (% LEL, %UEL).
It is essential to have sufficient information on the atmospheric composition in order to perform a reliable assessment.

## Slide 22
“Coward triangle” explosibility diagram (1)

## Slide 23
“Coward triangle” explosibility diagram (2)

## Slide 24
Explosibility diagram based on Fuchs/Culmann

## Slide 25: Addressing Secondary Explosion Risk
Underground incidents involving infrastructure damage
Is there a “window of opportunity”?
What are the critical information requirements?
Ideas for a resilient monitoring capability
Ideas for resilient communications

## Slide 26
The approach must offer reasonable prospects for surviving a local explosion or fire.
We speculate the use of roof-mounted monitoring ‘pods’…
  Located to provide strategic monitoring points
  Capable of measuring combustible gas levels
  Capable of detecting or confirming signs of life
  Facilitate personnel tracking, location and communications
The roof-mounted pods would be recessed (explosion-proof) and automatically or remotely activated after an incident.
Resilient Monitoring System

## Slide 27
Sensor Pod
Mine Passage

## Slide 28
Explosion
Sensor Pod
Mine Passage

## Slide 29
Damage to Infrastructure

## Slide 30
Sensor Pod now deployed
Damage to Infrastructure

## Slide 31
Deployment of Sensors

## Slide 32
Deployed Sensor Pod
CH4, CO etc
Deployment of Sensors
Notes: 32

## Slide 33
LF Transmission of Data
CH4, CO etc
Notes: 33

## Slide 34: Addressing Secondary Explosion Risk
Underground incidents involving infrastructure damage
Is there a “window of opportunity”?
What are the critical information requirements?
Ideas for a resilient monitoring capability
Ideas for resilient communications

## Slide 35
What happens if 100’s metres of entries are lost?
Survivability……..Challenge

## Slide 36
The approaches considered to offer the greatest potential for system survivability include:
  Fully integrated systems designed to use multiple transmission pathways
  Dynamically adaptive systems, using whatever transmission path survives
  ‘Hardening’ of system components (especially cables)
  Incorporation of redundancy, uninterruptible power supplies, and increased radio coverage.
A good practice to enhance resilience is to use a fibre-optic ring (using both shafts). However, the use of ring structures alone may not be sufficient - a fully ‘meshed’ structure represents a significant enhancement.
One proposed approach to resilient communications is to examine the application of low frequency mesh networks.
Resilient Communications

## Slide 37
Mine shafts/boreholes
Leaky Feeder
Primary path
Secondary path
Back-up link

## Slide 38
Mesh Networks:
More Nodes = Greater Reliability (multi-hopping, routed communications, short paths, lower RF power requirements)
Mesh = Self-configuring (self-organising, highly adaptable)
Mesh = Self-healing (automatic re-routing around failure)
Mesh = Redundancy (‘overdesigned’, multiple pathways)
Mesh = Scalable (hundreds+ network node capacity)

## Slide 39
LF Mesh Network
Deployed sensor pod
Mine communications network (cable)
Notes: 39

## Slide 40
Mine backbone network
Explosion-proof sensor pod
Other network nodes
Low frequency induction transmission through rock
Strategic mix of ‘drop-down’ environmental sensor pods supported by intermediate mesh nodes

## Slide 41
The benefit of a low frequency network is that the signal will travel through rock. However, the range is limited.
  For near-field induction communications the range in the worst case can follow a sixth-power law.
  That is, if it requires 10mW to transmit 50m then, to transmit ten times the distance, will require 106 times as much power, i.e. 10kW.
  Hopping 50m at a time requires only 100mW for a distance of 500m – not 10kW.
Low Frequency Mesh Network

## Slide 42
Because of the power v. range characteristic, a network of nodes is envisaged.
A proposed strategy is to use a high-resilience multi-hop transmission scheme, with an emphasis on survivability and automatic operation. This will provide the vital telemetry link from the measurement pods to the outside world.
The mesh network algorithms must be specially designed for LF use and to allow the data to be routed via alternative systems where appropriate – e.g. cable systems or the mine’s backbone network.
Low Frequency Mesh Network

## Slide 43
Summing up …
❶ There remain several issues in self-escape and rescue which would benefit from international research input.
  ❷ Mining and emergency management is increasingly technical and technology-intensive. Potentially significant benefits from monitoring and assessing new developments and innovations from other industry sectors.
  ❸ Research establishes an international outlook and access to network of technical specialists. Supports investigations and development of industry technical guidance.
  ❹ Example of possible approaches to secondary explosion risk reduction.
  ❺ IMRB is an excellent platform for technology transfer.

## Slide 44
Ladies and Gentlemen - Thank you