## Slide 1
The Importance of Providing Safe Breathable Air
in an Underground Mine Refuge Station
Randy Waylett
RANA Mine Refuge Systems
(sealed chamber)
Notes: Introduction & Read Title

## Slide 2
Notes: Refuge Stations have become an important component of Mine Safety design strategies. These Refuge Stations (which are designed to be sealed chambers), are strategically located underground and must provide a “Safe Haven” for mine workers and other persons who may be underground during a mine accident or critical safety event.
When people take refuge in a Refuge Station, one of the things they critically depend on is A Safe, Reliable Source of Breathable Air as well as Protection from hazardous gases that may be present in the mine.

## Slide 3: Standard Breathable Air
The air we breathe is made up of the following gases:
Nitrogen (78%)
Oxygen (21%)
Argon (0.94%)
Carbon Dioxide (0.04%)
Other trace gases (0.02%)
Notes: Standard breathable air (the air that surrounds us) is made up of two main components which are 78% Nitrogen and 21% Oxygen. The remaining 1% is made up of other trace gases, such as argon & carbon dioxide.

## Slide 4: Process of Normal Human Breathing
When we Inhale (breathe air in), our bodies consume oxygen and convert it to carbon dioxide. Exhaled air contains approximately 4.5% carbon dioxide.
Our bodies don’t do anything with the nitrogen or argon gas.
Notes: The process of breathing is something we don’t often think about because it’s normally an automatic process.
When we breathe in (inhale), our bodies absorb oxygen and produce a certain amount of carbon dioxide, which we (exhale). When the oxygen concentration of the breathable air becomes depleted, and more critically when the carbon dioxide concentration of the air increases to a high level our bodies will experience some ill affects. Combining these two effects at the same time becomes even more of a critical situation.
Let’s take a look at some charts.

## Slide 5: Oxygen Depletion
Concentration - % | Physiological Effects*
20.9% | Normal Concentration - no effect.
19.5% | Minimum Acceptable Value.
18.0% | Slight increase in breathing effort.
16.0% | Increase in pulse and breathing rate.
14.0% | Abnormal fatigue , emotional upset, impaired judgment, faulty coordination.
12.0% | Impaired respiration can cause cardiac damage, poor judgment, discomfort, vomiting, nausea.
< 10.0% | Unconsciousness, Death.
Notes: Read Through This Chart from slide

## Slide 6: Carbon Dioxide Accumulations
Concentration - PPM | Physiological Effects*
350 – 400 | Normal Concentration - no effect
5,000 | Slight increase in breathing rate. Time-Weighted Threshold Limit Value (TLV-TWA).
10,000 | Headache, Increased rate of breathing.
30,000 | Short-Term Exposure Limit (TLV-STEL).
50,000 | Panting, Discomfort, Intoxication in 30 minutes.
100,000 | Unconsciousness
>100,000 | Unconsciousness in one minute, Death.
Notes: Read Through This Chart from slide
So when considering the supply of air to a sealed chamber, such as a Refuge Station, we need to deal with both maintaining a safe Oxygen level, and a safe Carbon Dioxide level in the breathable air.
Goal to maintain the O2 level between 19.5% - 21.0%
Goal to maintain the CO2 level of less than 10,000 PPM (1%)
Usually it’s good design practise to provide two sources of breathable air for the mine Refuge Station. Therefore if one source should be compromised, you have an alternate source to rely on. In many mine safety jurisdictions, this requirement is becoming mandatory.
TLV – Threshold Limit Value - OSHA
TLV-TWA – average exposure on the basis of a 8 hour/day, 40 hour/week work schedule
TLV-STEL – spot exposure for a duration of 15 minutes, that cannot be repeated more than 4 times per day with at least 60 minutes between exposure periods.
TLV-C – absolute exposure limit that should not be exceeded at any time.
There are also PELs (Permissible Exposure Limits)
There are also RELs (Recommended Exposure Limits) - NIOSH

## Slide 7
Maximum number of persons the Refuge Station is designed for.
Design operational hours.
Two Critical Things to Know
Notes: When considering the Amount of Breathable Air required for a Refuge Station, there are two Critical Things we must know:
Maximum number of Persons the Refuge Station is designed for.
The Design Operational Hours of the Refuge Station.

## Slide 8: Sources of Breathable Air
Dead Air Space (based on physical size of the Refuge Station)
Mine Compressed Air Systems (outlet station in Refuge Station)
Oxygen Candles & Carbon Dioxide Absorbent Curtains (Manufacturer’s Specs.)
Breathable Air Systems (controlled supply of Oxygen & CO2 scrubber)
Notes: Today lets consider 4 Sources of Breathable Air.
They are:
Dead Air Space (based on physical size of the Refuge Station)
Mine Compressed Air Systems (air outlet centre/centres located in the Refuge Station)
Oxygen Candles & Carbon Dioxide Absorbent Curtains (Manufacturer’s Specs.)
Breathable Air Systems (which combine a controlled supply of Oxygen gas & CO2 scrubber)

## Slide 9: Dead Air Space
How much is required?
Industry Guideline: 2 cubic meters of standard air, per person, per hour.
Example: Refuge Station measures 5 meters wide X 10 meters long X 5 meters high Refuge Station volume is 250 cubic meters.
250 cubic meters of air / 2 cubic meters per person = 125 person hours of breathable air.
125 person hours / 10 persons = 12.5 hours of breathable air.
Notes: Dead Air Space
How much is Required?
Here we’ll use an industry Guideline of 2 cubic meters of standard air, per person, per hour.
Example: The Refuge Station’s physical size measures 5 meters wide x 10 meters long x 5 meters high. The volume of this particular Refuge Station is 250 cubic meters.
Therefore, 250 cubic meters of air / 2 cubic meters per person = 125 person hours of breathable air available.
If we have 10 persons occupying the Refuge Station, we would have 12.5 hours (125/10=12.5) of breathable air supply.
We would also need to assume the quality of the breathable air is acceptable.

## Slide 10: Mine Compressed Air System
How much mine compressed air is required?
General guideline: 5 m3/hr, per person (or 3 CFM)
10 persons x 5 m3/hr = 50 m3/hr (or 30 CFM)
Notes: Mine Compressed Air System
We need to ask the question,, How much mine compressed air flow do we need to maintain the breathable air concentration levels we require?
Typical guidelines are available from some of the workplace health & safety associations (OSHA, NIOSH, MSHA, etc.), but for our discussion today we are going to use a general guideline of 5 m3/hr (3 CFM) of compressed air per person to adequately replenish the oxygen and flush the carbon dioxide through the Refuge Station’s pressure relief valves.
Therefore if you have 10 persons occupying the Refuge Station, we need to maintain a flow of 50 m3/hr (30 CFM) of compressed air.

## Slide 11
Mine Compressed air outlet centre
Notes: Mine Compressed Air Outlet Centres should consist of :
Condensate drain (used during start-up; to clear the line)
Air line filters (ensure clean air supply)
Pressure Regulator
Flow regulator (fixed or adjustable)
Muffler (to lower noise level of outlet air)
Large Refuge Stations, over 20 persons, should have multiple mine compressed air outlet centres to limit the amount of air flow noise.
> 100 m3/h (60 CFM) … air flow becomes very noisy!
Mine Refuge Stations should have pressure relief valves to prevent the build up of pressure inside the Refuge Station.
Concerns when using a mine compressed air system? - May experience a broken or severed air line during an accident.
- May loose electrical power during accident and as a result you may loose your mine compressed air supply.

## Slide 12: Oxygen Candles & CO2 Absorbent Curtains
Amount of these supplies required, depends on the manufacturer’s specifications.
The dependability of using these items may be questionable and are becoming less commonly used for critical refuge station situations.
Notes: Oxygen Candles & CO2 Absorbent Curtains
Using these items to provide a breathable air supply source needs to be carefully considered.
Oxygen Candles will generate a certain amount of Oxygen gas over a specified period of time. Depending on the manufacturer’s specifications of these candles will determine how many candles you will require.
CO2 Absorbent Curtains will absorb a manufacturer’s specified amount of Carbon Dioxide, therefore the number of curtains required will also need to be calculated depending again on the number of persons occupying the Refuge Station and the amount of operational time required.
These product calculations involve a more complicated process. They are becoming less commonly used as a primary source, and are more commonly used for redundant purposes.

## Slide 13: Breathable Air Systems (Scrubber Systems)
Re-processes the Breathable Air
Adds Oxygen gas at a controlled flow rate
Removes the CO2
Notes: Breathable Air Systems (which also may be known as breathable air scrubber systems)
These manufactured systems are becoming more commonly used as a reliable source of breathable air (either primary or secondary).
RANA was the pioneer company who developed a system specifically for the mining industry, following a 1990 mine accident in Northern Canada.
These Breathable Air Systems re-process the air within the Refuge Station by adding Oxygen (at a controlled flow rate) and by removing the Carbon Dioxide through the scrubber bed.
These systems are typically powered by mine electrical power, or they may operate on battery back-up power provided within the system.
RANA can assist your Refuge Station design team to determine the number of units, size of units and the necessary supplies required based on the Refuge Station’s design.

## Slide 14
Breathable Air Centre
Refuge Station Air (high CO2)
Oxygen
Re-Processed Air
Notes: How The System Works.
There is an internal fan system (located in the base or bottom portion of the unit). These fans draw the Refuge Station air (indicated by the Red Arrows) and the oxygen gas (indicated by the Blue Arrows) into the scrubber beds.
The scrubber bed chemical (which is SL) adsorbs the carbon dioxide as the air flows through the scrubber beds.
As a result, the re-processed air (indicated by the Green Arrows) is exhausted from the Breathable Air System back into the Refuge Station.
These systems will maintain the breathable air at the acceptable, safe Oxygen and Carbon Dioxide levels within the Refuge Station, for the specified period of operational time.

## Slide 15
Notes: Picture of Typical Installation – we see a Breathable Air Centre installed in the Refuge Station

## Slide 16
Its extremely important that mine personnel are well trained on using these systems and that they carefully follow the manufacturer’s operational instructions.
Soda Lime Chemical
Oxygen Cylinder
Notes: These breathable air systems use a specific grade of Soda Lime Chemical which is the CO2 absorbent material and high pressure medical oxygen gas cylinders in the form of supplies.
Its extremely important that mine personnel are well trained on using these systems and that they carefully follow the manufacturer’s operational instructions.
These systems must be well maintained and properly equipped with the necessary supplies.

## Slide 17: RANA can help!
Questions?
Notes: As you can see there are lots of things to think about when planning for an adequate source (or sources) of Breathable Air for a mine Refuge Station.
RANA has over 20 years experience in this area and would be happy to provide any design assistance you may require.
I would encourage Mine Owners, Mine Design Engineers and Mine Safety Teams to think carefully about the Breathable Air sources of the Refuge Stations and take the necessary steps to ensure a safe, reliable breathable air supply is provided.
By doing this, it will provide safety confidence to your mine worker’s!
Thank you for allowing me to speak with you today. Do you have any questions or comments that you would like to make?

## Slide 18: Thank you!
Contact RANA:
Toll Free (in North America)
1-866-294-1409
Phone (outside North America)
1-204-272-5117
www.ranacaregroup.com/mine-refuge-systems
Notes: End of Presentation