## Slide 1
Optimizing Escapeway Ladders for Mine Rescue Purposes
International Mines Rescue Conference October 2013
Jay Gillon
Safescape North America

## Slide 2
Emergency Egress Ladders
Regulation of Escapeways
  Requirement of Escapeways
  Safety and usability of Escapeways
Evolution of Escapeway Systems
  Jackleg rising ladders
  Timber
  Steel Galvanized
  Fully Enclosed Polyethylene Ladders
Notes:   I would suggest you read this but reduce the text on the page to something like. * Escapeways are regulated, * Evolution of escapeway ladders. To be read: “The requirement for emergency egress from underground workings has long been regulated around the world.” AND “The safety and usability of these egresses can have a significant impact on the effectiveness of a mine rescue in the event of an emergency.

## Slide 3
Benefits of Ladderways compared to Alternative methods of escape*
Simple, self escape system
Relatively cheap to install and maintain
Reliable provided it is maintained in good condition
Relatively small opening and flexible design
*Raise Climbers, Vertical Shafts with Headframes, Hoists and Conveyances
Notes: You may wish to mention what you are comparing ladderways to when you comment on installation and maintenance costs, reliability etc. You are comparing against vertical shafts with headframes, hoists and conveyances or raise climbers.

## Slide 4
Ladderway Types
There are various types of ladders used in the mining industry. These include:
Timber
Jackleg Ladders
Steel Ladders
Steel Modular Ladder Cages
Fully Enclosed Polyethylene Ladders
Notes: Timber ladders are still used in places in the US. Americans and Canadians do handheld ladder rising (Aussie speak) bald headed raising (Yanky speak) differently to Australians so don’t harp on too much about Jack Leg Raising Ladders.

## Slide 5
Timber Ladders
Advantages
    Minimal training and skill needed to install
    Relatively inexpensive materials
Disadvantages:
  Timber tends to rot and steel corrodes over time (short lifespan or high maintenance)
  Uncomfortable to climb
  Heavy materials
  Must be installed from inside the shaft or raise
Notes: Timber ladders are still used in places in the US. Americans and Canadians do handheld ladder rising (Aussie speak) bald headed raising (Yanky speak) differently to Australians so don’t harp on too much about Jack Leg Raising Ladders.

## Slide 6
Jack Leg Raising Ladders
A ladder of simple construction utilized in jackleg raising and later used as permanent infrastructure in ladderways excavated by jackleg.
Very susceptible to corrosion
User is exposed to any falling material
High Risk Installation Procedure
Not well engineered for ladderways.
Notes: These ladders are often damaged during mining and it can be difficult to make them meet the MSHA guidelines or Canadian provincial regulations for escapeway ladders. Rocks tend to get caught underneath the rungs and when you climb the ladders they become loose and fall down the raise. Why it isn’t well engineered for mine rescue

## Slide 9
Steel Ladders
Made from round hollow sections
Easily affected by underground hyper saline water leading to rapid deterioration of their structural integrity.
Lighter and easier to move by operators which leads to less protection from corrosion.
Ladder user is exposed to elements
Ease of use for mine rescue personnel is one advantage of Steel Ladders
Notes: These ladders are easier to use to pull a stretcher up than the three stringer caged ladders with offset platforms. Because you can walk alongside the stretcher and lift it over the bolts and rungs and anything else it gets caught on.

## Slide 11
Steel Modular Ladder Cages
Designed as an improvement over steel ladders with the addition of a steel mesh cage to surround the user.
Added Protection for the User
Time Consuming to Install
High maintenance needs caused by corrosion and material properties
Notes: These are a nightmare to use for mine rescue purposes. When you are pulling a stretcher up you have to keep rigging up and rigging down with your haulage system and carry out the haulage within the ladderway because the offset platforms result in the haulage ropes rubbing on the platforms which is not good practice. Also the rungs and connections between sections and where you go past a platform, you have to manually manuever the stretcher which is awkward and physically quite tough. A lot of these designs work nicely to catch any rocks that fall down the raise and hold onto them at the rest platforms which is not good for when someone is walking above you and accidentally kick rocks down. Also the mesh caged ladders will occasionally catch the corner of your breathing apparatus when you’re climbing and this can be very annoying when you are fatigued and frustrated.

## Slide 15
Steel Modular Ladder Cages in Mine Rescue
Must carry out haulage within the Ladderway so haulage ropes do not rub on platforms
Manual maneuvering of stretcher adds physical strain to mine rescue personnel
Platforms can catch rocks and debris that are potential hazards to mine rescue personnel
Breathing apparatus can get caught on mesh ladders during climb
Notes: These are a nightmare to use for mine rescue purposes. When you are pulling a stretcher up you have to keep rigging up and rigging down with your haulage system and carry out the haulage within the ladderway because the offset platforms result in the haulage ropes rubbing on the platforms which is not good practice. Also the rungs and connections between sections and where you go past a platform, you have to manually manuever the stretcher which is awkward and physically quite tough. A lot of these designs work nicely to catch any rocks that fall down the raise and hold onto them at the rest platforms which is not good for when someone is walking above you and accidentally kick rocks down. Also the mesh caged ladders will occasionally catch the corner of your breathing apparatus when you’re climbing and this can be very annoying when you are fatigued and frustrated.

## Slide 16
Laddertube
Fully-enclosed polyethylene Ladderway.
Designed by an Australian mining engineer heavily involved with Australian mine rescue
Sealed polyethylene design protects user from exposure to water, salt or other mineral deposits
Made from lightweight non-corrosive materials.

## Slide 18
Sealed Polyethylene Ladders in Mine Rescue
Fully-enclosed polyethylene Ladderway protects user from mine environment
Straight line stretcher pull
No catch points for stretcher or Breathing apparatus
No place for breathing apparatus to get snagged
Bright yellow interior
Flat Step Profile

## Slide 19: Mine Rescue Video

## Slide 20
Notes: Smooth cage surface means the breathing apparatus doesn’t get caught on anything.
When you are climbing a ladder with a breathing apparatus donned you have very poor visibility, the bright yellow interior of Laddertube helps with this.
Also the flat step profile recruits those lower leg muscles where the rungs don’t which makes it easier to climb.

## Slide 21
Notes: Laddertube offers a straight line stretcher pull, where the haulage system can be positioned at the top of the ladderway making it easy to use.
There are no catch points for the stretcher to get caught on so the person moving with the casualty can focus on providing first aid support and encouragement rather than tossing the stretcher around and swearing about how crap the design of those steel ladders is.

## Slide 22
Safety Features
Fully enclosed travelway prevents dirt, rocks and salt water ingress and provides the user with a strong sense of security
Does not corrode or degrade over time
Rest Platforms added to meet user need
Fall arrest system included
Complies with AS1657 and MSHA requirements as well as various provincial regulations in Canada. Working to ensure Laddertube is acceptable in each province.

## Slide 23
Notes: Platform
Fall Arrest
Handrails

## Slide 24
Ease of Installation
Light weight
Simple tooling required
Very fast process
Majority of work during installation is done from outside of the raise
All consumables and installation plan provided.

## Slide 26
Notes: Safescape regularly contributes to various mine rescue competitions either by helping to organise events, sponsorship or provision of apparatus such as this confined space event at the Kalgoorlie surface mine rescue competition in 2011.

## Slide 27
Questions?
www.safescape.com
Notes: Feel free to upgrade the picture, and I don’t mean add a moustache!
What if I added a Goatee?