## Slide 1: Long Tunnel Rescues
Limitations of Rescue Teams due to Tunnel Design

## Slide 2: New Zealand
New Zealand is a narrow mountainous country with a rail network of 4,128 km (2,565 mi) narrow gauge rails
It has 150 tunnels

## Slide 3: Inherited Design
Source Christchurch City Library

## Slide 4: Otira
The tunnel passes under the Southern Alps, it opened on 4 August 1923.
The tunnel is unlit single track with a 1 in 33 grade rising 244 metres over its 8.5 kilometres (5.3 mi).
There are no formed walkways in the tunnel and minimal clearance either side of a train.
The tunnel is used by coal trains and a passenger (up to 600 passengers) train that has one return trip per day.

## Slide 5: Risk Tolerance
Risk of Fire
  Locomotives\Coal on Walls
Risk of Hypothermia
Risk of Asphyxia
Risk of CO Poisoning
Risk of Tunnel material collapse
Risk of Explosion

## Slide 6: Your Tunnels
Material Design
Escape Ways
Deluge Systems
Refuge Chambers
Lighting
Ventilation
  Characteristics
Temperature
Clearance
Contents of Tunnel
Access
Carriage Design
Locomotive/Generator Fire Suppression Systems
Back-up Power Supply
Location/Remoteness
Accommodation of Passengers
Double track
Coal Dust
Notes: Mont Blanc fire exacerbated by fans turned on by controllers

## Slide 7: Types of Rescue
Fire
Derail
Breakdown
Avalanche
Seismic
Collision

## Slide 8
Mont Blanc

## Slide 9: Mines Rescue V Fire Service
NZ Fire Service 150 Metres with high activity
NZMRS 4 Hrs - half-way into Otira on foot
High-rail vehicles (limitations in low oxygen)

## Slide 10: Risk Assessment
Determine risk tolerance level
Capability of rescue teams
Characteristics of tunnel design/construction & ventilation
Characteristics of tunnel traffic/cargo
Improvements needed

## Slide 11: Multi Agency Approach
Police
Fire
Mines Rescue
Rail Safety Regulator
Employee Safety Regulator
Tunnel Operator
Contribute to an Emergency Response Plan, Assist in the formation of a
Capital Improvement Plan